## Slide 1: Using Constructive Dual DP to Clear Water Markets in a Multi-Use Catchment: An Illustrative Example
Presented to EPOC Winter Workshop
Auckland, New Zealand, July 2012
by I Mahakalanda S Dye, R James, JF Raffensperger and E G Read

## Slide 2: An Integrated Water-Electricity Market Design for Mixed use, Multi-Reservoir System
Design and study a water market for mixed use, multi
reservoir systems that represents market dynamics and
agents’ learning behaviour.

## Slide 3: Objectives for this Presentation
To analyze mixed use of water in a multi-nodal inter-
temporal markets under uncertainty, with:
  Tributary, distributary, consumptive and non-consumptive flows.
  Catchment structure described as a tree, radiating from a single long term reservoir.
Long term optimisation/simulation via Stochastic CDDP uses
intra-period (deterministic) CDDP analysis to:
  Form net demand curve for water (DCW) at the reservoir.
  Form demand curves for water/flow at each node/arc.

## Slide 4: Single Reservoir Multi-node Model
0
3
1
4
5
6
8
2
9
10
7
Tributary flows
Distributary flows
Consumptive use
Non-consumptive use
Physical link
SUB-TREE 01
SUB-TREE 03
SUB-TREE 02
LONG TERM RESERVOIR

## Slide 5: Key Observations
Work inwards from the tips of the branches
back to the reservoir (node 0), irrespective of flow
direction, so:
  Downstream flow is negative sign if it is towards reservoir in tree.
  Some links allow bi-directional flow.
Represent consumptive uses & (dis)tributary
flows as net demands (DCW)
Quantities:
positive for ‘demand’.
negative for ‘supply’.
Prices:
sign remains unchanged.
Flow < 0
0
1
4
5
6
Flow < 0
Flow > 0
DCW
DCW
Flow <> 0
DCW
Flow > 0
Flow > 0
DCW
DCW
DCW
DCR

## Slide 6: Key Observations
Arc bounds truncate demand curves.
Non-consumptive uses create Demand Curve for Flow (DCF)
Pumping/generation adds cost/benefit to arc flow in physical flow direction.
DCF adjusts prices in DCW passed along arc:
DCF adds to DCW prices if physical flow is away from reservoir, but
DCF subtracts from DCW prices if flow is toward reservoir, in tree.
0
1
4
5
6
Flow < 0
Flow > 0
Flow <> 0
Flow > 0
Flow > 0
DCF <0
DCF>0

## Slide 7: Nodal Demand Curve for Water (DCW)
8
Tributary flows
Distributory flows
Consumptive use
6
5
4
Truncate (arc cap)
Tributary flow
DCW80
+h
Distributary flow
Consumptive use
+h
DCW80
DCW60
[1 , 2]

## Slide 8: Non-consumptive Flow
DCF6-50
+v
8
Non-consumptive use
6
5
4
T(DCW60)
Truncated DCW from node 6
DCW after adjusting for DCF passing down to node 5

## Slide 9: Method
0
1
+h
+h
+v
DCW04
+h
Consumptive
Distributary
Tributary
DCF1-00
DCR00
DCW10
T(DCW10)
Work inwards, towards the long term reservoir, forming Nodal DCW for each node:
  Adding nodal DCW to DCW’s passed “in” along any arcs from nodes further out in tree
  Truncating for feasibility and
  Adjusting for non-consumptive arc costs/benefits.

## Slide 10: Numerical Illustration: NDCW (Sub-Tree 01)
0
3
1
4
5
6
7
2
9
10
8
8
7
5
1
6
4

## Slide 11: Stochastic Inter-temporal Optimization (market- clearing)
Apply CDDP to form “Demand Curve for Water” from
reservoir (DCW0t)in each period
Use this as “Demand Curve for Release” (DCR) in
stochastic CDDP model of Dye et al:
Dye S., Read E. G., Read A.R., and Starkey S.R., 2012,Easy implementation of generalised stochastic CDDP models for market simulation studies, 4th IEEE and Cigré International Workshop on Hydro Scheduling in Competitive Markets, Norway.
Full Markov version with state dependent bids/tributaries and “informed” intra-period release policy requires us to run intra-period CDDP (or modify base solution) once for each state.

## Slide 12: Summary and Future Directions
Single reservoir intra-period multi nodal catchment model (this talk)
Single reservoir Inter-temporal stochastic (Markov) multi nodal catchment model (Dye et al)
Multi-reservoir intra-period multi nodal catchment model (by efficient adaptation of base solution)
Multi-reservoir Inter-temporal stochastic (Markov) multi nodal catchment model
Market operation under different management and ownership regimes (using multi-agent approach)