## Slide 1
Modelling reserve scarcity under RTP
7th September 2018
EPOC Winter Workshop 2018

## Slide 2: Outline
Current dispatch and pricing
Real-time pricing
Risk/reserve modelling:
  Potential issues with current risk/reserve modelling
  Proposed risk/reserve modelling

## Slide 3: Current dispatch and pricing schedule
Real-time dispatch schedule used to dispatch energy and reserves
Real-time pricing schedule produces indicative prices every five minutes
Final ex post price schedule, based on 30-minute trading periods, determines prices on which the market is settled
Scarcity prices might be resolved during final price determination

## Slide 4: Real-time pricing
Final pricing schedule will cease to exist
Prices will be determined every 5 minutes according to the real time dispatch schedule
Half-hourly settlement prices to be calculated using the ‘5-minute’ prices
Scarcity prices, if they exist, will remain and will impact settlement prices

## Slide 5: Real-time pricing – proposed energy scarcity modelling
5% of load at $10,000/MWh
15% of load at $15,000/MWh
80% of load at $20,000/MWh

## Slide 6: Real-time pricing – current reserve scarcity modelling
Constraint Violation Penalties (CVPs) are used to price reserves
Current CVP for 6s (FIR) and 60s (SIR) reserve is $100,000/MWh
Under a scarcity situation, reserves might be priced out of the market allowing plant offering reserves to provide energy instead. Inadequate reserve provision then leads to load shedding
⇒ How to determine the optimal value for reserve CVPs?

## Slide 7: Issues with current reserve scarcity modelling
If reserve CVPs are too low ⇒ available expensive supply may not be used but reserve violation is preferred if there are multiple risk setters
If reserve CVPs too high ⇒ energy violation might be preferred by SPD instead of violating reserve requirement and keeping the lights on

## Slide 8: Simplified risk/reserve modelling
HVDC risk:
Generation risk:

## Slide 9: Simplified risk/reserve modelling
Total cleared reserve:
Matching of requirements and availability:

## Slide 10: Simplified risk/reserve modelling
Objective function:

## Slide 11: Simplified risk/reserve modelling

## Slide 12: SPD: Energy and reserve price basics
Energy price: the marginal cost to supply the next 1 MW of demand
Reserve price: the benefit of 1 MW of ‘free’ reserve in the system.
Under a normal situation, the definition of energy and reserve price is straight-forward
Under a tight supply situation, the energy cost may impact the reserve price and the reserve cost may impact the energy price

## Slide 13: Potential issues with current reserve scarcity modelling

## Slide 14: Case study 1
One risk setter and both reserve classes are constrained
The next 1 MW of demand is supplied by a risk setting plant (or HVDC)
If scarcity occurs in both reserve markets, the virtual marginal cost of FIR and SIR is the reserve CVP:
Assuming CVPFIR and CVPSIR = $10,000/MWh
⇒ Priceenergy > $20,000/MWh ⇒ Load shedding is a better option (Or is it?)
Skip example

## Slide 15: Case study 1 example (inputs)
North Island
Demand: 1650 MW
South Island
Demand: 1000 MW
Ignoring transmission losses, net free reserve, HVDC ramp up, HVDC capacity, reserve sharing and reserve requirement in SI
Energy CVP = $10,000/MWh
FIR CVP = $10,000/MWh
SIR CVP = $10,000/MWh

## Slide 16: Case study 1 example (inputs)
IL FIR: 100 MW @ $100/MWh
IL SIR: 100 MW @ $200/MWh
Energy: 1500 MW @ $100/MWh
FIR: 200 MW @ $20/MWh
SIR: 250 MW @ $30/MWh
North Island
Demand: 1650 MW
South Island
Demand: 1000 MW
Energy: 3000 MW @ $0.01/MWh

## Slide 17: Case study 1 example (results)
IL FIR: 100 MW @ $100/MWh
IL SIR: 100 MW @ $200/MWh
Energy: 1300 MW @ $100/MWh
FIR: 200 MW @ $20/MWh
SIR: 200 MW @ $30/MWh
North Island
Demand: 1650 MW
South Island
Demand: 1000 MW
Energy: 1300 MW @ $0.01/MWh
HVDC
NI  SI
300 MW

## Slide 18: Case study 1 example (results)
IL FIR: 100 MW @ $100/MWh
IL SIR: 100 MW @ $200/MWh
Energy: 1300 MW @ $100/MWh
FIR: 200 MW @ $20/MWh
SIR: 200 MW @ $30/MWh
North Island
Demand: 1650 MW
50 MW energy shortage
South Island
Demand: 1000 MW
Energy: 1300 MW @ $0.01/MWh
HVDC
NI  SI
300 MW
FIR price: $100/MWh
SIR price: $9899.99/MWh
Energy price: $10,000/MWh

## Slide 19: Case study 1 example (modified CVPs)
North Island
Demand: 1650 MW
South Island
Demand: 1000 MW
Ignoring transmission losses, net free reserve, HVDC ramp up, HVDC capacity, reserve sharing and reserve requirement in SI
Energy CVP = $10,000/MWh
FIR CVP = $4,500/MWh
SIR CVP = $4,500/MWh

## Slide 20: Case study 1 example (results)
IL FIR: 100 MW @ $100/MWh
IL SIR: 100 MW @ $200/MWh
Energy: 1300 MW @ $100/MWh
FIR: 200 MW @ $20/MWh
SIR: 200 MW @ $30/MWh
North Island
Demand: 1650 MW
South Island
Demand: 1000 MW
Energy: 1350 MW @ $0.01/MWh
HVDC
NI  SI
350 MW
FIR price: $4,500/MWh 50 MW FIR deficit
SIR price: $4,500/MWh 50 MW SIR deficit
Energy price: $9,000.01/MWh

## Slide 21: Case study 2
Three supply sources (A, B, C) are constrained by either reserve class
Assuming FIR supply is constrained (scarce)
Assuming CVPFIR = $10,000/MWh, marginal energy cost at A, B and C is insignificant and marginal SIR price is very low ⇒ Priceenergy ≈ $3333.33/MWh
⇒ Energy supply source with marginal cost > $3333.33/MWh will not be cleared but a reserve deficit is preferred by the model
Skip example

## Slide 22: Case study 2 example (inputs)
North Island
Demand: 1510 MW
South Island
Demand: 1000 MW
Ignoring transmission losses, net free reserve, HVDC ramp up, HVDC capacity, reserve sharing and reserve requirement in SI
Energy CVP = $10,000/MWh
FIR CVP = $10,000/MWh
SIR CVP = $10,000/MWh

## Slide 23: Case study 2 example (inputs)
North Island
Demand: 1510 MW
South Island
Demand: 1000 MW
Energy: 350 MW @ $0.01/MWh
FIR: 20 MW @ $1/MWh
SIR: 30 MW @ $1/MWh
Energy: 350 MW @ $0.02/MWh
FIR: 20 MW @ $2/MWh
SIR: 30 MW @ $2/MWh
Energy: 100 MW @ $5,000/MWh
Energy: 1000 MW @ $100/MWh
FIR: 200 MW @ $3/MWh
SIR: 300 MW @ $3/MWh
Energy: 3,000 MW @ $0.01/MWh

## Slide 24: Case study 2 example (results)
North Island
Demand: 1510 MW
South Island
Demand: 1000 MW
Energy: 230 MW @ $0.01/MWh
FIR: 20 MW @ $1/MWh
SIR: 30 MW @ $1/MWh
Energy: 230 MW @ $0.02/MWh
FIR: 20 MW @ $2/MWh
SIR: 30 MW @ $2/MWh
Energy: 0 MW @ $5,000/MWh
Energy: 800 MW @ $100/MWh
FIR: 200 MW @ $3/MWh
SIR: 200 MW @ $3/MWh
Energy: 1,250 MW @ $0.01/MWh
HVDC
NI  SI
250 MW

## Slide 25: Case study 2 example (results)
North Island
Demand: 1510 MW
South Island
Demand: 1000 MW
Energy: 230 MW @ $0.01/MWh
FIR: 20 MW @ $1/MWh
SIR: 30 MW @ $1/MWh
Energy: 230 MW @ $0.02/MWh
FIR: 20 MW @ $2/MWh
SIR: 3 MW @ $2/MWh
Energy: 0 MW @ $5,000/MWh
Energy: 800 MW @ $100/MWh
FIR: 200 MW @ $3/MWh
SIR: 200 MW @ $3/MWh
Energy: 1,250 MW @ $0.01/MWh
HVDC
NI  SI
250 MW
Energy price: $3334.35/MWh
FIR price: $10k/MWh
SIR price: $3/MWh
10 MW of FIR deficit

## Slide 26: Case study 2 example (modified CVPS)
North Island
Demand: 1650 MW
South Island
Demand: 1000 MW
Ignoring transmission losses, net free reserve, HVDC ramp up, HVDC capacity, reserve sharing and reserve requirement in SI
Energy CVP = $10,000/MWh
FIR CVP = $15,000/MWh
SIR CVP = $15,000/MWh

## Slide 27: Case study 2 example (results)
North Island
Demand: 1510 MW
South Island
Demand: 1000 MW
Energy: 220 MW @ $0.01/MWh
FIR: 20 MW @ $1/MWh
SIR: 30 MW @ $1/MWh
Energy: 220 MW @ $0.02/MWh
FIR: 20 MW @ $2/MWh
SIR: 30 MW @ $2/MWh
Energy: 30 MW @ $5,000/MWh
Energy: 800 MW @ $100/MWh
FIR: 200 MW @ $3/MWh
SIR: 190 MW @ $3/MWh
Energy: 1,240 MW @ $0.01/MWh
HVDC
NI  SI
240 MW
Energy price: $5,000/MWh
FIR price: $14,996.96k/MWh
SIR price: $3/MWh

## Slide 28: Issues with current reserve scarcity modelling
If reserve CVPs are too low ⇒ available expensive supply may not be used but reserve violation is preferred if there are multiple risk setters
If reserve CVPs too high ⇒ energy violation might be preferred by SPD instead of violating reserve requirement and keeping the lights on

## Slide 29: Desirable outcomes during scarcity in real-time pricing
Reserve/risk violation is preferable to load shedding
Reserve/risk violation should be limit at certain level
Reserve price reflecting the risk(s) that are covered
The current reserve scarcity modelling can’t achieve all of the above

## Slide 30: Proposed risk/reserve modelling
HVDC risk:
Generation risk:

## Slide 31: Proposed risk/reserve modelling
Matching of requirements and availability:
Risk Violation Tranches Allocation:

## Slide 32: Proposed risk/reserve modelling
Objective function:

## Slide 33: Proposed risk/reserve modelling

## Slide 34: Example of risk violation tranche limits and CVPs
Violation limits (MW) | FIR CVP ($/MWh) | SIR CVP ($/MWh)
10 MW | 4,500 | 4,000
10 MW | 7,500 | 7,000
10 MW | 9,500 | 9,000
20 MW | 12,000 | 11,000
1,000 MW | 15,000 | 15,000

## Slide 35: Case study 1
One risk setter and both reserve classes constrained
Assuming CVPenergy = $10,000/MWh and the risk binding supply source is cheap enough
⇒ Can violate the risk up to 10 MW before load shedding occurs

## Slide 36: Case study 2
Three supply sources (A, B, C) are constrained by 6s reserve class (FIR)
Assuming CVPenergy = $10,000/MWh and the risk binding supply sources are cheap enough
Assuming the other non-risk setting supply sources are available at $5000/MWh
⇒ Risk violation up to 10 MW occurs at A, B, C in the order of energy cost and frees up 30 MW of energy before the $5,000/MWh supply is required

## Slide 37: Conclusion
The multi-step risk violation model seems to do the trick
Still need to determine the limits and cost of risk violation tranches
Soft limit on reserve offer prices